## Slide 1: Network Security: TLS/SSL
Tuomas Aura
T-110.5241 Network security Aalto University, Nov-Dec 2013

## Slide 2: Outline
Diffie-Hellman key exchange (recall from earlier)
Key exchange using public-key encryption
Goals of authenticated key exchange
TLS/SSL architecture
TLS handshake (!)
TLS record protocol
TLS trust model

## Slide 3: Diffie-Hellman key exchange
Recall from previous lecture

## Slide 4: Signed DH with nonces and key confirmation
Signed Diffie-Hellman with nonces and key confirmation:
1. A → B: A, B, NA, gx, SA(“Msg1”, A, B, NA, gx), CertA
2. B → A: A, B, NB, gy, SB(“Msg2”, A, B, NB, gy), CertB, MACSK(A, B, “Responder done.”)
3. A → B: A, B, MACSK(A, B, “Initiator done.”)
SK = h(NA, NB, gxy)
Ok to reuse the exponents x and y

## Slide 5: Ephemeral Diffie-Hellman
Perfect forward secrecy (PFS): session keys and data from past sessions is safe even if the long-term secrets, such as private keys, are later compromised
  Even participants themselves cannot recover old session keys
  Called “perfect” for some historical reason; the word means nothing specific
General principle of implementing PFS: create a new temporary public key pair for each key exchange and afterwards discard the private key
Common way to implement PFS is ephemeral DH (DHE): both sides use a new DH exponents in every key exchange and forget the exponent values afterwards
Cost of ephemeral Diffie-Hellman: random-number generation for new x and y, exponentiation for the DH public keys gx and gy, and cannot cache and reuse previously computed gxy if communicating with the same peer
Typical trade-off: replace DH exponents periodically, e.g. once in a day or hour, and use nonces to create a fresh session key: SK = h(gxy, NA, NB)

## Slide 6: Key exchange using public-key encryption

## Slide 7: PK encryption of session key
Public-key encryption of the session key:
1. A → B: A, PKA
2. B → A: B, EA(SK)
SK = session key
EA(…) = encryption with A’s public key
Note: This protocol
is not secure
like this. Please read further.

## Slide 8: Impersonation and MitM attacks
The protocol again:
1. A → B: A, PKA
2. B → A: B, EA(SK)
SK = session key
EA(…) = encryption with A’s public key
Same impersonation and man-in-the-middle attacks are possible as in unauthenticated Diffie-Hellman:
A → T(B): A, PKA // Trent intercepts the message
T(B) → A: B, EA(SK) // Trent spoofs the message

## Slide 9: Authenticated key exchange
Authenticated key exchange with public-key encryption:
1. A → B: A,B, NA, CertA
2. B → A: A,B, NB, EA(KM), SB(“Msg2”,A,B,NA,NB,EA(KM)), CertB, MACSK(A, B, “Responder done.”)
3. A → B: A,B, MACSK(A, B, “Initiator done.”)
SK = h(NA, NB, KM) // why nonces and not SK = KM?
KM = random key material (random bits) generated by B
CertA = certificate for A’s public encryption key
EA(…) = encryption with A’s public key
CertB = certificate for B’s public signature key
SB(…) = B’s signature
MACSK(…) = MAC with the session key
Typically RSA encryption and signatures because the same RSA keys can be used for both
Somewhat realistic protocol

## Slide 10: Goals of authenticated key exchange

## Slide 11: Basic security goals
Create a good session key:
  Secret i.e. known only to the intended participants
  Fresh i.e. never used before
  Separation of long-term and short-term secrets: long-term secrets such as private keys or master keys are not compromised even if session keys are
Authentication:
  Mutual i.e. bidirectional authentication: each party knows with whom it shares the session key
  Sometimes only one-way i.e. unidirectional authentication
Optional properties:
  Entity authentication: each participant knows that the other is online and participated in the protocol
  Key confirmation: each participant knows that the other knows the session key (implies entity authentication)
  Perfect forward secrecy: compromise of current secrets should not compromise past session keys
  Contributory key exchange: both parties contribute to the session key; neither can decide the session-key alone

## Slide 12: Advanced security goals
Non-repudiation
  A party cannot later deny taking part (usually not an explicit goal)
Plausible deniability
  No evidence left of taking part (usually not an explicit goal either)
Integrity check for version and algorithm negotiation
  Increases difficulty of version roll-back attacks
Identity protection:
  Sniffers cannot learn the identities of the protocol participants
  Usually, one side must reveal its identity first, making it vulnerable to active attacks against identity protection
Denial-of-service resistance:
  The protocol cannot be used to exhaust memory or CPU of the participants
  It is not easy to spoof packets that prevent others from completing a key exchange
  The protocol cannot be used to flood third parties with data

## Slide 13: Protocol engineering
Network is a distributed system with many participants
Computer networking is about protocols
  Protocol = distributed algorithm
  Algorithm = stepwise instructions to achieve something
Security is just one requirement for network protocols
  Cost, complexity, performance, deployability, time to market etc. may override some security properties
Like the design of cryptographic algorithms, security engineering requires experienced experts and peer scrutiny
  Reuse well-understood solutions such as TLS; avoid designing your own protocols
The most difficult part is understanding the problem
  Must understand both security and the application domain
  When the problem is understood, potential solutions often become obvious

## Slide 14: TLS/SSL

## Slide 15: TLS/SSL
Originally Secure Sockets Layer (SSLv3) by Netscape in 1995
Originally created to facilitate web commerce:
  Encrypting credit card numbers and passwords on the web
  Fast adoption because built into web browsers
A historical note:
  First, there was resistance against SSL, especially in the IETF. It was believed that IPsec would eventually replace SSL. SSL was considered bad because it lowered the motivation to adopt IPsec
  Now SSL/TLS is the dominant encryption standard
Standardized as Transport-Layer Security (TLS) by IETF [RFC 5246]
  Minimal changes to SSLv3 implementations but not interoperable with it

## Slide 16: TLS/SSL architecture (1)
Encryption and authentication layer added to the protocol stack between TCP and applications
End-to-end security between client and server, usually web browser and web server

## Slide 17: TLS/SSL architecture (2)
TLS Handshake Protocol — authenticated key exchange
TLS Record Protocol — block data delivery
General architecture of security protocols: authenticated key exchange + session protocol
TSL specifies separate minor “protocols”:
  Alert — error messages
  Change Cipher Spec — turn on encryption or update keys

## Slide 18: Cryptography in TLS
Key-exchange mechanisms and algorithms organized in cipher suites
  Negotiated in the beginning of the handshake
Example: TLS_RSA_WITH_3DES_EDE_CBC_SHA
  RSA = handshake: RSA-based key exchange
  Key-exchange uses its own MAC composed of SHA-1 and MD5
  3DES_EDE_CBC = data encryption with 3DES block cipher in EDE and CBC mode
  SHA = data authentication with HMAC-SHA-1
TLS mandatory cipher suites: TLS_DHE_DSS_WITH_3DES_EDE_CBC_SHA (TLS 1.0)
  DHE_DSS = handshake: ephemeral Diffie-Hellman key exchange authenticated with DSS* signatures
TLS_RSA_WITH_3DES_EDE_CBC_SHA (TLS 1.1)
TLS_RSA_WITH_AES_128_CBC_SHA (TLS 1.2)
SHA-1 and MD5 in the handshake replaced with a negotiable MAC algorithm in TLS 1.2
Insecure cipher suites: TLS_NULL_WITH_NULL_NULL TLS_RSA_EXPORT_WITH_DES40_CBC_SHA

## Slide 19: TLS handshake

## Slide 20: TLS handshake protocol
Runs on top of TLS record protocol
Negotiates protocol version and cipher suite (i.e. cryptographic algorithms)
  Protocol versions: 3.0 = SSLv3, 3.1 = TLSv1
  Cipher suite e.g. DHE_RSA_WITH_3DES_EDE_CBC_SHA
Performs authenticated key exchange
  Several different key exchange mechanisms supported (typically RSA and DHE)
  Often only the server is authenticated

## Slide 21: TLS Handshake (DH)
Client | Server
ClientHello | 
 | ServerHello Certificate* ServerKeyExchange* CertificateRequest* ServerHelloDone
Certificate* ClientKeyExchange CertificateVerify* ChangeCipherSpec Finished | 
 | ChangeCipherSpec Finished
Application data | Application data
Optional, client typically unauthenticated.
Client D-H key etc.
Server D-H key and signature etc.
1. Negotiation 2. Authentication 3. Key exchange 4. Key confirmation 5. Start session
Protocol version, server nonce, cipher suite
Protocol versions, client nonce, cipher suites
Server certificate
Optional
signature
Key confirmation
Key confirmation
Encrypted and MAC’ed session data

## Slide 22: TLS handshake
1. C → S: ClientHello
2. S → C: ServerHello, Certificate, [ ServerKeyExchange ], [ CertificateRequest ], ServerHelloDone
3. C → S: [ Certificate ], ClientKeyExchange, [ CertificateVerify ], ChangeCipherSpec, Finished
4. S → C: ChangeCipherSpec, Finished
[Brackets] indicate fields not needed in one-directional authentication

## Slide 23: TLS_DHE_DSS handshake
1. C → S: Versions, NC , SessionId, CipherSuites
2. S → C: Version, NS , SessionId, CipherSuite CertChainS g, n, gy, SignS(NC, NS, g, n, gy) [ Root CAs ]
3. C → S: [ CertChainC ] gx [ SignC(all previous messages including NC, NS, g, n, gy, gx) ] ChangeCipherSpec MACSK (“client finished”, all previous messages)
4. S → C: ChangeCipherSpec MACSK("server finished“, all previous messages)
pre_master_secret = gxy
master_secret = SK = h(pre_master_secret, “master secret”, NC, NS)
The Finished messages are already protected by the new session keys
1. Negotiation 2. Ephemeral Diffie-Hellman 3. Nonces 4. Signature 5. Certificates 6. Key confirmation and negotiation integrity check

## Slide 24: TLS Handshake (RSA)
Client | Server
ClientHello | 
 | ServerHello Certificate* ServerKeyExchange* CertificateRequest* ServerHelloDone
Certificate* ClientKeyExchange CertificateVerify* ChangeCipherSpec Finished | 
 | ChangeCipherSpec Finished
Application data | Application data
Optional, client typically unauthenticated.
Key material encrypted to server
Not needed
1. Negotiation 2. Authentication 3. Key exchange 4. Key confirmation 5. Start session
Protocol version, server nonce, cipher suite
Protocol versions, client nonce, cipher suites
Server certificate
(RSA)
Optional
signature
Key confirmation
Key confirmation
Encrypted and MAC’ed session data

## Slide 25: TLS_RSA handshake
1. C → S: Versions, NC , SessionId, CipherSuites
2. S → C: Version, NS , SessionId, CipherSuite CertChainS [ Root CAs ]
3. C → S: [ CertChainC ] ES(pre_master_secret), [ SignC(all previous messages including NC, NS, ES(…)) ] ChangeCipherSpec MACSK (“client finished”, all previous messages)
4. S → C: ChangeCipherSpec MACSK("server finished“, all previous messages)
ES = RSA encryption (PKCS #1 v1.5) with S’s public key from CertChainS
pre_master_secret = random number chosen by C
master_secret = SK = h(pre_master_secret, “master secret”, NC, NS)
Finished messages are already protected by the new session keys
1. Negotiation 2. RSA 3. Nonces 4. Signature 5. Certificates 6. Key confirmation and negotiation integrity check

## Slide 26: Nonces in TLS
Client and Server Random are nonces
Concatenation of a real-time clock value and random number:
struct {
uint32 gmt_unix_time;
opaque random_bytes[28];
} Random;

## Slide 27: Session vs. connection
TLS session can span multiple connections
  Client and server may cache the session state and master_secret
  Client sends the SessionId of a cached session in Client Hello; otherwise zero
  Server responds with the same SessionId if session found in server cache; otherwise with a fresh value
When session is reused, new session keys derived from old master_secret and new nonces
Change of IP address does not invalidate cached sessions
Session tickets [RFC 5077]:
  Server can send the session state data (ticket) to the client
  Client sends the ticket back to the server when reconnecting
  Ticket is encrypted and authenticated with a secret key know only to the server  client cannot modify data
  Not implemented by all browsers

## Slide 28: TLS renegotiation attack
TLS client or server can initiate “renegotiation handshake” i.e. new handshake to refresh session keys
In 2009, a protocol flaw was found:
  MitM attacker intercepts a TLS connection from honest client; lets the client in the beginning of the handshake
  Attacker executes a TLS handshake with the honest server and sends some data to the server over this TLS connection
  Attacker forwards the (still unauthenticated) connection from the client to the server over its own TLS connection
  Honest client executes the TLS handshake with the server; server thinks it is renegotiation; attacker loses ability to decrypt the data after ChangeCipherSpec, but continues to forward the connection
What did the attacker achieve? Attacker inserted its own data to the beginning of the connection
  E.g. consider applications where the client sends commands first and finally authorizes them by entering its password
Solved by RFC 5746
Surprising because TLS/SSL is one of the most analyzed protocols and no major protocol-level flaws have been found since 1995

## Slide 29: TLS record protocol

## Slide 30: TLS record protocol
For write (sending):
  Take arbitrary-length data blocks from upper layer
  Fragment to blocks of ≤ 4096 bytes
  Compress the data (optional)
  Apply a MAC
  Encrypt
  Add fragment header (serial number SN, content type, length)
  Transmit over TCP server port 443 (https)
For read (receiving):
  Receive, decrypt, verify MAC, decompress, defragment, deliver to upper layer

## Slide 31: TLS record protocol - abstraction
Abstract view: EK1 (data, HMACK2(SN, content type, length, data))
Different encryption and MAC keys in each direction
  All keys and IVs are derived from the master_secret
TLS record protocol uses 64-bit unsigned integers starting from zero for each connection
  TLS works over TCP, which is reliable and preserves order. Thus, sequence numbers must be received in exact order

## Slide 32: TLS Applications
Originally designed for web browsing (HTTPS)
  Client typically unauthenticated
New applications:
  Any TCP connection can be protected with TLS
  The SOAP remote procedure call (SOAP RPC) protocol uses HTTP as its transport protocol. Thus, SOAP can be protected with TLS
  TLS-based VPNs
  EAP-TLS authentication and key exchange in wireless LANs and elsewhere
Many of the new applications require mutual authentication

## Slide 33: Related reading
William Stallings. Network security essentials: applications and standards, 3rd ed. chapters 7.1-7.2; 4th ed. chapter 5
William Stallings. Cryptography and Network Security, 4th ed.: chapters 17.1-17.2
Kaufmann, Perlman, Speciner. Network security, 2nd ed.: chapters 11, 19
Dieter Gollmann. Computer Security, 2nd ed. chapter 13.4; 3rd ed. chapter 16.5

## Slide 34: Exercises
Use a network sniffer (e.g. Netmon, Ethereal) to look at TLS/SSL handshakes. Can you spot a full handshake and session reuse? Can you see the lack of identity protection?
What factors mitigate the lack of identity protection in TLS?
How would you modify the TLS handshake to improve identity protection? Remember that the certificates are sent as plaintext and SessionId is also a traceable identifier.
Why do most web servers prefer the RSA handshake?
Consider removing fields from the TLS DHE and RSA key exchanges. How does each field contribute to security?
How to implement perfect forward secrecy with RSA?
Why have the mandatory-to-implement cipher suites in TLS changed over time?
How many round trips between client and server do the TLS DHE and RSA key exchanges require? Consider also the TCP handshake and that certificates may not fit into one IP packet.
Why is the front page of a web site often insecure (HTTP) even if the password entry and/or later data access are secure (HTTPS)? What security problems can this cause?
What problems arise if you want to set up multiple secure (HTTPS) web sites behind a NAT or on a virtual servers that share only one IP address? How does the server name extension (RFC 6066) help?
If an online service (e.g. webmail) uses TLS with server-only authentication to protect passwords, is the system vulnerable to offline password cracking?